## Slide 1
CHIRP: Climate Hyperspectral InfraRed Product
From Larrabee Strow’s ROSES activity:
Convert AIRS, CrIS, IASI to a common spectral spectral response function (SRF)
Correct for instrumental radiance offsets
Provides long-term radiance continuity over different instruments
Allows use of a single forward model (Radiative Transfer Algorithm) for retrievals
Common SRF for AIRS/CrIS and IASI (1:30 and 9:30 equator crossings)
Applications
  Gridded (time/space) radiance products (“L1G”)
  Geophysical retrievals (anomalies, trends) directly from all-sky radiance anomaly/trends. (See talk by L. Strow)
  OLR trends directly from radiance trend retrievals (See talk by Sergio DeSouza-Machado)
  Use for Level 2 retrievals? Only way to mitigate radiance calibration difference among instruments and to achieve common sensitivity (both for radiances and RTA)